## Slide 1: Parameter design for investigating the effect of group behaviour on crowd dynamics
Group behaviour model
Parameter contribution
Parameter design for investigating the effect of group behaviour
Notes: The effect of group behaviour on crowd dynamics.-> to extract useful information (interaction between group) for evacuation plan (should escape group or alone, group by group) according to parameters of each group;
In various design layout- , flow rate average, flow rate of each group.
Discussion about which design layouts suitable, plans suit for group having maximum group cohesion, or group speed., guidance for evacuation plan
-----------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
What is data in panic situations useful for human crowd modelling? Hard because data in panic is rare, not fix. Previous studies almost investigate general data for context detection at dense place; or data in normal situation; or machine learning for abnormal behaviour detection model when disaster already happened- not for panic situations. While panic situations- group of pedestrians escape together rather escape alone), with learder or group of different ped parameter distribution. This study focuses on the instinct characteristic of group behaviour in simulations when they interact in order to extract useful information before disasters happen.
Discussion about which design layouts suitable, plans suit for maximizing group cohesion, or group speed. – Group contains pedestrians having different parameter to those of others.
The data of extracting interaction between groups in which groups have different parameters to those of others (group have maximize group cohesion, group have low speed) .
Guidance for each group evacuation; adding stochastic information dynamic context

## Slide 2: 1. Group behaviour model
A pedestrian p moving in a group
= | 
The repulsive force created by pedestrian q on pedestrian p
Attraction force illustrates that pedestrian p wants to move close to pedestrian q
Notes: Literally, the higher value means pedestrian p feel more uncomfortable and want to move further away from pedestrian q caused by the increase of repulsive force.
The exponent function is used to describe that the repulsive force decrease exponentially if is high.
The higher value makes attraction force increase since and represent radii of pedestrians p and q, and ≤ . Factor is the unit vector pointing from pedestrian p to pedestrian q to illustrate the force direction making pedestrian p move close to pedestrian q.
Literally, the higher 𝐵_𝑟𝑒𝑝 value means pedestrian p feel more uncomfortable and want to move further away from pedestrian q caused by the increase of repulsive force.
The exponent function is used to describe that the repulsive force decrease exponentially if 𝑑_𝑝𝑞 is high.
The higher 𝐵_𝑎𝑡𝑡 value makes attraction force increase since 𝑅_𝑝 and 𝑅_𝑞 represent radii of pedestrians p and q, and 𝑅_𝑝+𝑅_𝑞 ≤ 𝑑_𝑝𝑞. Factor (𝑢_𝑝𝑞 ) ⃗ is the unit vector pointing from pedestrian p to pedestrian q to illustrate the force direction making pedestrian p move close to pedestrian q.

## Slide 3: 1. The analysis of parameter contribution- Experiment Design
Group population size = 5
Each parameter is uniformly sampled 2000 times
16000 parameter combinations are used to simulate the model
Each combination is simulated 10 times which have different placements
Parameter combinations share the same 10 placements
In each simulation time, group members use the same parameter values
Monitoring period:
  remove the first 10 seconds
  measure the group cohesion degree and speed until one group member has escaped

## Slide 4: Parameter Analysis-Group cohesion degree
Correlation testing
Sobol indices analysis
Notes: Anti group,
Correlation testing,
the overall effects of one parameter on the variance of model’s output
Tuning verify parameter, keep the same scenario
At base parameter

## Slide 5: Parameter Analysis-Group average speed
Correlation testing
Sobol indices analysis
Notes: Correlation testing,
Anti group,
Tuning verify parameter

## Slide 6: Parameter Analysis-Verification
Group cohesion verification by Interaction Range parameter
Group speed verification by Velocity parameter

## Slide 7: Parameter Analysis-Discussion
Group cohesion degree depends on Repulsive Interaction Range
Group average speed depends on Desired Speed
This conclusion works as considering group members have the same parameter values
Notes: which represents the average distance to group center’s mass,

## Slide 8: 2.1. Parameter design- hypothesises regarding repulsive force
Hypothesis (H1) Do pedestrians having less repulsive force caused by group members than the those force caused by out-of-group members give the difference in flow rates, average speed and cohesion degree?
How to formulate that effect?
Group of pedestrians have
    lower Interaction Range (B) for in-group members
    higher Interaction Range (B) for out-of-group members
  Group of pedestrians have
    lower Interaction Strength (A) for in-group members
    higher Interaction Strength (A) for out-of-group members
where 0 1
Notes: Hoorgedoorn found that, children <elderly< adults
(easily accept other pedestrians standing closer)

## Slide 9
(H2)Whether two groups of pedestrians having different attraction force to its group members give the difference in flow rates, average speed and cohesion degree?
How to formulate that effect?
2.1. Parameter design- hypothesises regarding attraction force
    Group A has higher Attraction Range than those value of group B
    Group A has higher Attraction Strength than those value of group B

## Slide 10: 2.1. Parameter design- hypothesises regarding group velocity
(H3) Whether two groups of pedestrians having different desired velocity give the difference in flow rates, average speed and cohesion degree?
How to formulate that effect?

## Slide 11: 2.2. Group effect measurement algorithm
Step1: Define design layouts and group’s context (population size, placements)
Step2: Define parameters according to hypothesis
Step3: Observation analysis
  Measure flow rates of groups
  Measure overall flow rate
  Measure environment information(crowd density, crowd behaviour near by obstacles)
  Compare the above results to those values in scenarios without group behaviour or the difference between in-of-group and out-of-group members
Step4: Modelling the change of crowd dynamics according the each hypothesis
Notes: Contain different layouts, placements of group, number of pedestrians
Propose hypothesises measurement by turning parameters
Observation: return data (crowd density-heatmap, flow rates, crowd pressure)
Analysis and verification